## Slide 1: WIRELESS INTERFACE
This document is strictly confidential to its recipients
in TCC and should not be copied, distributed or reproduced in whole or in part.
TOSHIBA Home AC Control
IoT
By TCTC
HOW TO ADD AIR CONDITIONERS

## Slide 2
Wireless adapter connectivity
One AC can be controlled by maximum 5 users
A user can control up to 10 ACs
All 5 users can control all 10 ACs

## Slide 3
How to add AC?
Register Email address | User name | Password | Wireless adapter | Remark
Father@toshiba | Father1 | a12345 | No.1 - 10 | Need to add AC
Father@toshiba | Mother1 | b12345 | No.1 - 10 | Can set different user name and password, No need to add AC, Automatically pair
Father@toshiba | Peter1 | c12345 | No.1 - 10 | Can set different user name and password, No need to add AC, Automatically pair
Father@toshiba | Sarah1 | d12345 | No.1 - 10 | Can set different user name and password, No need to add AC, Automatically pair
Father@toshiba | Jean12 | e12345 | No.1 - 10 | Can set different user name and password, No need to add AC, Automatically pair
5 user control 1 AC
By Using the same register email address

## Slide 4
Add AC 1st time
AP mode
Add AC
If the wireless adapter is not in AP mode press “SETUP” button 1 time
AP mode
When first time adding AC please follow installation manual and make sure you wireless adapter is AP mode(Access point mode 2 LED will on)
AP mode 2 LED will on

## Slide 5
Re-add AC : Problem case
Re-add AC when change Wi-Fi router or Change register email address or Change wireless adapter to use with another A/C
Delete AC from mobile app
AP mode
Add AC
Failed due to server and adapter still keep sending old provisioning signal
When user re-add AC(wireless adapter) after 1st paring
1
2
By press “SETUP” button until AP mode
AP mode
You might need to press “SETUP” button several time until AP mode
( 2 LED on),
because of adapter keep retry connected to Cloud
And some time all 3 LED on happened, must press “RESET” and try to repress “SETUP “again
Special mode

## Slide 6
*** if press until all 3 LED ON for long time adapter will go to test mode then LED will not change the state to AP mode. This case press RESET ***
Re-add AC : Correct method
TCTC recommendation re-add AC method
Delete AC from mobile app
Factory reset + AP mode
By pressing “SETUP” button and hold for 5 seconds. Immediately release when all 3 LED ON
Add AC
Add AC complete
When user re-add AC(wireless adapter) after 1st paring
1
2
all 3 LED will show for
3 seconds, then automatic go to AP mode
AP mode
Press SETUP too long time

## Slide 7
Re-add AC : Backup method
Incase of Adapter already deleted from mobile app without any Factory reset first
Delete AC from mobile app
Add AC
When user re-add AC(wireless adapter) after 1st paring
Factory reset
1
2
AP mode
By press “SETUP” button until AP mode
You might need to press “SETUP” button several time until AP mode
( 2 LED on),
because of adapter keep retry connected to Cloud
And some time all 3 LED on happened, must press “RESET” and try to repress “SETUP “again
Special mode
AP mode
*** if press until all 3 LED ON for long time adapter will go to test mode then LED will not change the state to AP mode. This case press RESET ***
By pressing “SETUP” button and hold for 5 seconds. Immediately release when all 3 LED ON
all 3 LED will show for
3 seconds, then automatic go to AP mode
AP mode
Press SETUP too long time